## Slide 1: Robust Multi-objective Iterative Learning Control
Tong Duy Son
Promoters
Prof. Jan Swevers
Prof. Goele Pipeleers
September 2016

## Slide 2
1st try

## Slide 3
2nd try

## Slide 4
3rd try

## Slide 5
1. perform
2. analyze
3. do again (and better)
3rd try

## Slide 6: Repetitions
1. perform
2. analyze
3. do again (and better)

## Slide 7: Repetitions in industry
vehicle testing
batch processes
industrial robots
semiconductor

## Slide 8: Repetitions in industry
vehicle testing
batch processes
industrial robots
semiconductor
control system

## Slide 9: Challenges
Goal of this thesis
Improve the control system
Exploit ‘repetition’
Improvements in
Robustness
Precision
Fast
Energy efficiency

## Slide 10
Desired output: pick an object from A to B
Question: What input should you apply?
input
desired output
Consider a robot arm in a factory
Sketch of Control

## Slide 11
Desired output: pick an object from A to B
Question: What input should you apply?
input
desired output
knowledge of the system!
Sketch of Control

## Slide 12: Sketch of Control
FeedbackController
Feedforward Controller
Feedback
Feedforward

## Slide 13: Sketch of Control
Model uncertainty
Disturbance
Transient response, lag
Non-minimum phase
Highly dependent on accuracy of the model
Disturbance has to be known
Feedback
Feedforward

## Slide 14: Sketch of Control
Model uncertainty
Disturbance
Transient response, lag
Non-minimum phase
Highly dependent on accuracy of the model
Disturbance has to be known
Feedback
Feedforward
feedforward
feedback
no control
feedforward
feedback
no control

## Slide 15: Sketch of Control
Model uncertainty
Disturbance
Transient response, lag
Non-minimum phase
Highly dependent on accuracy of the model
Disturbance has to be known
Feedback
Feedforward
feedforward
feedback
no control

## Slide 16: Repetitions in industry
same task and same performance
hundreds to thousands times a day

## Slide 17: Revisit: Challenges
Goal of this thesis
Improve the control system
Exploit ‘repetition’
Iterative learning control (ILC): improves control performance by incorporating information from previous trials

## Slide 18: Iterative Learning Control (ILC)
Iterative learning control (ILC): improves control performance by incorporating information from previous trials
)

## Slide 19: Main contributions
Multi-objective frequency domain ILC
Lifted system ILC: analysis and synthesis
Robust norm-optimal ILC

## Slide 20: Main contributions
Multi-objective frequency domain ILC
Lifted system ILC: analysis and synthesis
Robust norm-optimal ILC

## Slide 21
Introduction (1)
Most ILC designs reply on a two-step sequential problem formulation and the design procedures are usually heuristic:
Design L then design Q:
  L as model-inversion or phase-lead type
  Q as a low-pass filter: depends on designed
Design Q then design L:
  design Q
  find L that optimize the learning speed
Iterate the previous 2 designs
The design is not optimal while costly and time consuming!
)
designed controller: (Q,L)

## Slide 22
Introduction (2)
Hard to incorporate multi-objective intuitively
Robustness (unmodeled dynamics, uncertain parameter…)
  Robustness vs tracking performance
  Unknown: robustness and tracking performance vs learning speed
  have 1 month training have 4 year training (i.e. for Olympic): more difficult attempts
Input constraints
Trade-offs between the objectives

## Slide 23
Methodology
Design Q, L simultaneously using optimization
Accounts for the trade-off designs
Approach:
First, specify the desired performance, input constraints, and robustness conditions. Next, design ILC controller (Q, L) to optimize the convergence (learning) speed with the given specifications
minimize convergence speed
Q,L
subject to robust performance
robust convergence
input constraints

## Slide 24
Methodology
Design Q, L simultaneously using optimization
Accounts for the trade-off designs
Approach:
First, specify the desired performance, input constraints, and robustness conditions. Next, design ILC controller (Q, L) to optimize the convergence (learning) speed with the given specifications
minimize convergence speed
Q,L
subject to robust performance
robust convergence
input constraints
non-convex,
hard to solve!

## Slide 25
Methodology
Design Q, L simultaneously using optimization
Accounts for the trade-off designs
Approach:
First, specify the desired performance, input constraints, and robustness conditions. Next, design ILC controller (Q, L) to optimize the convergence (learning) speed with the given specifications
minimize convergence speed
Q,L
subject to robust performance
robust convergence
input constraints
non-convex,
hard to solve!
reformulated as
a linear program

## Slide 26
Advantages (1)
Multi-objective
optimality
computation
flexibility
intuition
multi-objective

## Slide 27
Advantages (1)
Multi-objective
and their trade-offs:
  convergence speed
  input constraints
  robust convergence
  robust performance
optimality
computation
flexibility
intuition
multi-objective
Notes: aa

## Slide 28
Advantages (2)
Optimality
no 2-step and heuristic design
(Q, L) is simultaneously generated using optimization
noncausal ILC controller
optimality
computation
flexibility
intuition
multi-objective
reliable as a result of a linear program
Computation

## Slide 29
Advantages (4)
Flexibility
controller type: FIR, IIR, PID...
different objectives:
minimize tracking performance
Q,L
subject to convergence speed
robust convergence
input constraints
no parametric model is required, only FRFs
continuous and discrete
selecting interested frequencies: i.e. for noise and disturbance rejection.
optimality
computation
flexibility
intuition
multi-objective

## Slide 30
Advantages (5)
Intuition
Use conventional control system terminologies: sensitivity function, bandwidth
optimality
computation
flexibility
intuition
multi-objective

## Slide 31
Advantages (5)
Intuition
Use conventional control system terminologies: sensitivity function, bandwidth
optimality
computation
flexibility
intuition
multi-objective
Automated design possible
Multi-objective
ILC algorithm
system model (FRFs)
performance specs. (bandwidth)
ILC controller
(and learning speed)

## Slide 32
Validation
Validate the proposed ILC designs: simulations and experiments
Validate the multi-objective trade-offs
Compare with existing designs
Control Development
Simulation & Experimental Validation

## Slide 33
Validation
Control Development
Simulation & Experimental Validation
tracking performance function (sensitivity function)
convergence (learning) speed function

## Slide 34
Validation
Control Development
Simulation & Experimental Validation
convergence speed vs
tracking performance with
2 different designs
convergence speed vs
input constraints
red: no constraint

## Slide 35
Validation: trade-off designs
Control Development
Simulation & Experimental Validation
Select the desired controller:
desired tracking performance
desired learning speed
level of uncertainty

## Slide 36: Main contributions
Multi-objective frequency domain ILC
Lifted system ILC: analysis and synthesis
Robust norm-optimal ILC

## Slide 37
Introduction
Consider multiple objectives as previous,
but investigate time domain using lifted system representation
of finite trial length.
(Q,L) are matrix variables
Study robust analyses
Proposes ILC syntheses (designs)
)
designed controller: (Q,L)

## Slide 38
Robustness
Robust monotonic convergence and robust performance analyses
an LMI (or BMI) problem
i.e.
Both unstructured and structured uncertainty are considered

## Slide 39
Synthesis
(for short/moderate trial lengths)
Synthesis I: Optimize convergence speed
Synthesis II: Optimize tracking error
)
designed controller: (Q,L)
minimize convergence speed
L
subject to an LMI problem
minimize tracking error
Q
subject to an LMI problem

## Slide 40
Validation
Control Development
Simulation & Experimental Validation
XY-wafer stage with linear motor

## Slide 41: Main contributions
Multi-objective frequency domain ILC
Lifted system ILC: analysis and synthesis
Robust norm-optimal ILC

## Slide 42
Introduction
Norm-optimal ILC is an efficient way to design the optimal ILC input:
is the cost function w.r.t the nominal model (no uncertainty model is accounted)
analytical solution (noncausal, time-varying controller)
has to sacrifice a lot tracking performance to obtain robustness
minimize

## Slide 43
Methodology
obtain both robustness and high tracking performance
deal with input constraints
efficient computation
Approach:
optimize the worst-case cost function:
minimize sup
subject to input constraints

## Slide 44
Methodology
obtain both robustness and high tracking performance
deal with input constraints
efficient computation
Approach:
optimize the worst-case cost function:
minimize sup
subject to input constraints
non-convex
problem

## Slide 45
Methodology
obtain both robustness and high tracking performance
deal with input constraints
efficient computation
Approach:
optimize the worst-case cost function:
minimize sup
subject to input constraints
minimize
,
subject to input constraints
non-convex
problem
reformulated as
a convex problem

## Slide 46
Advantages
obtain robustness w.r.t. cost function (proved):
deal with input constraints
efficient computation
high tracking performance?

## Slide 47
Advantages
obtain robustness w.r.t. cost function (proved):
high tracking performance?
Considering the same cost function:
  if the classical norm-optimal ILC diverges, the proposed robust ILC still converges.
  if the classical norm-optimal ILC converges, the robust ILC also converges to similar tracking performance but with lower convergence speed

## Slide 48
Advantages (cont.)
deal with input constraints
efficient computation
the selection of weight matrices is not critical as other norm- optimal ILC designs.
the proof of the equivalence to an adaptive norm-optimal ILC (trial-varying controller) can be used to avoid solving optimization if needed (i.e. when convergence is already obtained).

## Slide 49
Validation
Control Development
Simulation & Experimental Validation
Validate the proposed ILC designs: simulations and experiments
Compare with classical (robust and non-robust) norm-optimal ILC: accurate model, inaccurate model

## Slide 50
Validation
Control Development
Simulation & Experimental Validation
Validate the proposed ILC designs: simulations and experiments
Compare with classical (robust and non-robust) norm-optimal ILC: accurate model, inaccurate model
accurate model
inaccurate model
red: classical norm-optimal ILC
blue: proposed ILC
black: other robust design

## Slide 51
Validation
Control Development
Simulation & Experimental Validation
Validate the proposed ILC designs: simulations and experiments
Compare with classical (robust and non-robust) norm-optimal ILC: accurate model, inaccurate model
accurate model

## Slide 52: Main contributions
Multi-objective frequency domain ILC
Lifted system ILC: analysis and synthesis
Robust norm-optimal ILC

## Slide 53: Summary
Robust ILC: robustness and high tracking performance, frequency and time domain
Multiple objectives and their trade-offs
Efficient computation
Extensive simulation and experimental validations:
guideline to select the suitable controller

## Slide 54: Future works
Multivariable (MIMO) systems
Different classes of uncertainty modelling
Robust ILC nonlinear optimization
ILC for different purposes: energy optimal, time-optimal…
Applications (human in the loop, distributed systems…)

## Slide 55
Thank you!
More detailed information: https://tongduyson.github.io/publication.html

## Slide 56
Conservative: small
Evaluate the original constraints:
and
using both simulation and experiments for different system models)
The differences are small hence
small conservative.
page 69 (thesis)

## Slide 57: (near) Future works
Multivariable (MIMO) systems
performance condition:

## Slide 58: (near) Future works
2-order controllers generated from
the optimization problem: